## Slide 1
Controller and data acquisition circuit:
Starts/Stops pump.
Opens/Closes valve.
Collects pressure/flow/pulse/temp data
User interface:
Displays pump/valve operation.
Displays blood pressure and pulse.
Computes and displays EnDys score.
Cuff
Mass Flow
Sensor
6
Pump
8
Boolean
Deflation
Valve
5
Electrical connection
Fluidic connection
Gage
Pressure
Sensor
2
Absolute
Pressure
Sensor
3
Temperature
Sensor
4
Pulse
Sensor
1
Restriction
Valve
7
1. Sparkfun SEN-11574
2. Sensortechnics HCEM500GUH9P3
3. Sensortechnics HDIB002AUY8H5
4. Sensirion STS21 (also purchased evaluation kit EK-H5 for convenient testing)
5. Parker X-1-05-S-F (also purchased X-2-05-S-F if we need to deal with higher pressure difference)
6. Sensirion EM1NR4R0V_1A
7. Bird precision (I bought a range, spanning a few orifice sizes and outer diameters, so we can choose the right one)
8. Xavitech P1500-GAS-12V or the P200 which Justin already has (also bought the flow calibration unit)
Component names